## Slide 1
PYNQ-Z2 Multiband Audio Processing Accelerator
A Python reference and HLS FIR core for four-band dynamic-range compression
193
FIR taps per low-pass filter
2.00 ms
96-sample FIR group delay at 48 kHz
449 cycles
HLS schedule per sample
Subtractive crossover
Three linear-phase low-pass filters form four adjacent bands. The bands sum to the input delayed by 96 samples before compression.
Edges: 500 Hz, 1 kHz, 2 kHz
b1 = LP500
b2 = LP1000 - LP500
b3 = LP2000 - LP1000
b4 = delayed input - LP2000
HLS core resource use
Out-of-context implementation, 100 MHz clock constraint
Chart: 
| LUT | Flip-flops | DSP | BRAM
Device resources | 7.5 | 5.2 | 91.8 | 36.8
Python run: 10.58 s audio processed in 100.7 ms on the local desktop (best of 5). This is not an FPGA speedup comparison.
Block-by-block board path. PL 0.317 µs/sample vs ARM scipy C 6.199 µs (19.5×; Q1.15 vs float64; no NEON).
Bypass: 144k samples, zero mismatches. Live mic -> core -> headphone: 1.00x real time (40 s, bit-exact), still bit-exact across live per-band gain changes (66 s, 6 writes; heard). PYNQ 2.7.0 + Vivado/Vitis HLS 2020.2.
Notes: Sources: src/python/band_design.py; data/results/baseline_metrics.md (local Python run, 2026-10-01); data/results/impl_metrics.md (193-tap HLS out-of-context implementation); data/results/accel_cpu_vs_fpga.md and data/results/fir_audio_loop_run_20261001.txt (board results). The 449-cycle and resource chart figures are core-only out-of-context results. The core is also integrated in the board audio overlay; board throughput is 0.317 µs/sample for the PL core versus 6.199 µs/sample for ARM scipy (Q1.15 vs float64, a 19.5x ratio, and not a maximum CPU comparison). Bypass passed on 144,000 captured samples. Live microphone monitoring works as of 2026-10-15: a 40 s duplex run carried 4,000 blocks at 1.00x real time with a bit-exact 960,000/960,000 self-check, in-core level rms median 107 / peak 24,076, and the operator heard the processed voice. Scope: that run used 0.0 dB on all four band gains, so it demonstrates the audio path rather than the four-band effect, and about 18 blocks were dropped over the 40 s because the audio IP has no DMA. The four-band effect itself was demonstrated in a second 2026-10-15 run: six live writes to the band gains inside one continuous 66 s stream, one band alternating 0.0 dB and -41.9 dB, all applied, self-check still bit-exact 960,000/960,000 across eight gain changes, 1.00x, operator heard several distinct changes (data/results/fir_gain_ab_run_20261015.txt). A symmetric +6/0/0/-6 setting was tried first and was inaudible because total loudness barely changed. fir_audio_loop.py still produces the four comparison wav files block by block; fir_live.py runs the continuous live duplex stream. Toolchain: PYNQ 2.7.0, Vivado/Vitis HLS 2020.2. The 2.00 ms value is FIR group delay only.