## Slide 1
PYNQ-Z2 Multiband Audio Processing Accelerator
A Python reference and HLS FIR core for four-band dynamic-range compression
193
FIR taps per low-pass filter
2.00 ms
96-sample FIR group delay at 48 kHz
449 cycles
HLS schedule per sample
Subtractive crossover
Three linear-phase low-pass filters form four adjacent bands. The bands sum to the input delayed by 96 samples before compression.
Edges: 500 Hz, 1 kHz, 2 kHz
b1 = LP500
b2 = LP1000 - LP500
b3 = LP2000 - LP1000
b4 = delayed input - LP2000
HLS core resource use
Out-of-context implementation, 100 MHz clock constraint
Chart: 
| LUT | Flip-flops | DSP | BRAM
Device resources | 7.5 | 5.2 | 91.8 | 36.8
Python run: 10.58 s audio processed in 100.7 ms on the local desktop (best of 5). This is not an FPGA speedup comparison.
Scope: HLS values are core-only OOC results. Custom-core board integration, live audio, and end-to-end latency are still pending.
Notes: Sources: src/python/band_design.py; data/results/baseline_metrics.md (local Python run, 2026-10-01); data/results/impl_metrics.md (193-tap HLS out-of-context implementation). Resource percentages and HLS schedule are core-level results, not board audio measurements. The 2.00 ms value is FIR group delay only. Custom-core board integration is pending.